## Slide 1
Marin Ljuban
Compliance checking for construction project data with linked data
LBD-CG presentation

## Slide 2: Introduction
The goal is to asess how IFC could be lifted to a more generic ontology, enabling connection of BIM models to other information models such as GIS, Electronic Document Management (EDM), Systems Engineering (SE), Monitoring & Control (M&C)… The planned process can be summed up in 3 main steps:
Taxonomy
Attributes
Properties
The existing IfcOWL ontology will be queried for classes and used as a base for creation of classes of the new OTL and connected to the ISO 17632 ontology
TASK
TASK
SCOPE
The IfcOWL ontology will be queried for attributes of classes queried in step 1. These attributes will be appended to newly created classes but aligned to the EN 17632.
The IFC properties are not available directly in the IfcOWL, but in XML. The properties will be converted to RDF with the help of RML and appended to the OTL classes aligned to the EN 17623.
Relations
When parsing the actual IFC file, the IFC relations considered in the scope of the thesis (spatial containment & decomposition) will be replaced with equivalent concepts from the new EN ontology.
  Creation of the object type library (OTL) from the IfcOWL and XML Property Set files and connecting it to the new EN ontology
  Development of script that parses IFC-STEP file and produces an OTL-compliant dataset
  Creating SHACL ruleset to enable dataset checking based on local, national or EU regulation

## Slide 3: State of the art in digital building permitting
Notable efforts in the European Union
The building design process Is complex and fragmented, with 10 to 12 disciplines involved on average – manual compliance checking with low accuracy and high cost
Only 27% of economies use a digitized e-submission based process, OECD leading with 48%
ACC researched for over 50 years, with significant uptake in the last 7 years – connected with the increase of adoption of digital representation of building and geospatial data across the world
Complex and multi-factored problem; technical and non-technical factors- this research deals with technical part
Relevant findings
Academic research is steadily growing since 2015 – pilot deployment gained momentum in 2022
Technological solutions should be based on the open standards and easy to use
Despite alignment efforts, there is little chance for one-fits-all solution; for mass deployment flexibility and customization is key
Preparation of 3D city models and geo info
Pre-consultation & preliminary analysis
Conversion 3D city model/geo info
Application review (content)
Eight step framework for digital permitting (Noardo et al., 2022)
Rule interpretation & digitalization
BIM modelling & IFC export
Application review (formal)
Completion & notification

## Slide 4: EN 17632, BIM – Semantic modelling and linking (SML)
Newly published (March 31st) standard enabling more efficient management of projects and the resulting assets. The document specifies how organizations in the built environment should apply Linked Data to best suit their needs. The application should help integration of complex information models (BIM, GIS, EDM etc.)
Guidelines. Easy to implement.
Contains a generic construction ontology, as well as guidelines about modelling patterns and application of levels of semantic modeling capability for different use cases (vocabulary, basic/advanced ontology)
At the time of beginning of the research the EN 17632 ontologies were not available. Therefore, the dutch predecessor (nen2660) is used. It is believed that the EN ontology would only contain minor difference from the nen2660.
Focus on building elements, properties (attributes) and relations. Possible to express additional relationships e.g. materials (nen2660:matter) and system connections (nen2660:Port)

## Slide 5: OTL Taxonomy

## Slide 6: Parsing IFC-STEP

## Slide 7: Test projects

## Slide 8: IFC-STEP Validation
File name | Number of entities in the LBD dataset | Number of entities in the thesis dataset
Arch1 | 2740 | 2741
Arch2 | 251 | 252
Mech | 492 | 493

## Slide 9: SHACL & To be done
Expressing IFC attributes with the QUDT units (prescribed in EN 17632); parsing of the IFC attributes
Conversion of IFC properties contained in XML Property sets to OWL (RML); parsing of the properties, both predefined as well as user-defined properties
Creation of SHACL shapes to validate some of the entities for compliance with regulations – testing of different available tools, e.g. RASE Markup, NLP processing for automation of SHACL shapes
Remarks about the IFC structure
Consistency in enumeration naming needed
Standard & Elemented case as enumeration or as entity?
How to map same spatial entities from different models of the same project (e.g. architectural & MEP)
Relevancy of attributes, properties and the units – aligning with QUDT

## Slide 10
Questions?
Thank you for the attention!