## Slide 1
Let’s add occupants
to our digital twins!
Alex Donkers – PhD Candidate at Eindhoven University of Technology – a.j.a.donkers@tue.nl
Dujuan Yang, Bauke de Vries, Nico Baken

## Slide 4
The current amount of light is not sufficient for this task
The probability that :JaneDoe suffers visual discomfort is 94%

## Slide 5: While buildings should be designed for their occupants, many buildings fail to satisfy their expectations.
How to monitor building performance?
How to integrate the occupant?
How to create parallel intelligence?

## Slide 6: How to monitor building performance?

## Slide 7
Indoor Environmental Quality
Thermal comfort
Acoustic comfort
Visual comfort
Air quality
Natural ventilation
CO2 level
Particulate matter
Mechanical ventilation
Reverberation time
Background noise level
Communication privacy
Mean radiant temperature
Relative humidity
Surface temperature
Air velocity
Geometry of rooms and elements
Building topology
Weather information
Occupant preferences
Activity level
Glare
Natural light
Artificial light
Visual privacy
Sociodemographics
Mood
Clothing level
Metabolic rate

## Slide 8: Mean radiant temperature
Ts,2
Ts,3
Ts,1
Ts,4
Ts,5
As,2 *
Thermal transmittance
Indoor air temperature
Indoor air velocity
Indoor heat transfer coefficient
Outdoor air temperature
Outdoor air velocity
Outdoor relative humidity
Sun intensity
Sun azimuth
Height of the sun
Surface tilt
Surface azimuth

## Slide 9
TOPOLOGY
Rooms
Elements
How they relate to each other
STATIC PROPERTIES
Geometry
Material characteristics
DYNAMIC PROPERTIES
Sensor data
Weather data
Challenge
Integrate the heterogeneous information related to building performance assessments.

## Slide 10: Building Topology Ontology (BOT)

## Slide 11: Approaches to describe property values
GRAPH DATABASE
GRAPH DATABASE
TIME-SERIES DATABASE
S01,21,1630575705
S01,21,1630575706
S01,22,1630575709
:Building
:Room
:Sensor01
:Temperature
:Observation01
“21”
“1630575705”
“21”
“1630575706”
:Observation02
:value
:value
:time
:time
:hasSpace
:hasSensor
:observes
:hasResult
:hasResult
:Building
:Room
:Sensor01
:Temperature
:hasSpace
:hasSensor
:observes
:timeSeriesReference
“InfluxDB-S01”
READ MORE
Tang et al. (2019)

## Slide 12: Static and dynamic properties
ONTOLOGIES FOR DYNAMIC PROPERTIES
Semantic Sensor Network Ontology (SSN)
Sensor, Observation, Sample and Actuator (SOSA)
Smart Applications REFerence Ontology (SAREF)
Brick
ONTOLOGIES FOR STATIC PROPERTIES
Ontology for Property Management (OPM)
BIM Design Ontology (BIMDO)
Building Product Ontology (BPO)
:Property
Value
:PropertyState
:FeatureOfInterest
:Sensor
:Property
:FeatureOfInterest
:Observation
Value
:Result

## Slide 13: Properties: four levels of detail
FeatureOfInterest
Property
Execution
PropertyState
^^xsd:decimal
Unit
FeatureOfInterest
Property
PropertyState
^^xsd:decimal
Unit
FeatureOfInterest
Property
^^xsd:decimal
Unit
FeatureOfInterest
^^cdt:datatype
hasResult
hasProperty
Level 1
1 class, 1 datatype property
Level 2
2 classes, 1 object property,
1 datatype property
Level 3
3 classes, 2 object property,
1 datatype property
Level 4
4 classes, 3 object property,
1 datatype property

## Slide 14: Building Performance Ontology (BOP)
bop:Executor
bop:Property
bop:FeatureOfInterest
bop:Execution
bop:Result
bop:hasFeatureOfInterest/
bop:isFeatureOfInterestOf
bop:executedBy/
bop:performsExecution
bop:hasExecutedProperty/
bop:hasExecution
hasProperty min 1/
isPropertyOf min 1
bop:executesOn/
bop:isExecutedBy
Value
bop:hasValue max 1
Unit
bop:hasSimpleUnit max 1
bop:Unit
bop:hasUnit max 1/
bop:isUnitOf
bop:Database
bop:hasExternalDatabase/
bop:isDatabaseOf
bop:hasSubProperty/
bop:isSubPropertyOf
bop:PropertySet
bop:containsProperty /
bop:ispartOfPropertySet
TimeOfGeneration
prov:generatedAtTime
^^xsd:dateTime
bop:DataPoint
bop:Procedure
bop:usesProcedure/
bop:isUsedFor
bop:implementsProcedure/
bop:implementedBy
bop:hasSubExecutor/
bop:isSubExecutorOf
bop:Platform
bop:hosts min 1/
bop:isHostedBy max 1
bop:hasComplexProperty/
bop:isComplexPropertyOf
bop:hasExecutionState/
bop:isExecutionStateOf
bop:hasPropertyState/
bop:isPropertyStateOf
bop:hasSimpleExecutionState
bop:hasSimpleProperty
bop:hasSimplePropertyState
rdfs:subClassOf
owl:ObjectProperty
owl:DatatypeProperty
rdfs:Class
rdfs:Literal
bop:Input
bop:Output
bop:UserDefined
ID
bop:hasID max 1
Class
Literal
rdfs:subPropertyOf bop:hasResult
rdfs:subPropertyOf bop:isResultOf
rdfs:subPropertyOf bop:hasSimpleResult
bop:hasDataPoint/
bop:isDataPointOf

## Slide 15
RULES AND REGULATION
PMV
PPD
PYTHON
Real-time building performance monitoring
STATIC PROPERTIES
Geometry
Material characteristics
DYNAMIC PROPERTIES
Sensor data
Weather data
TOPOLOGY
Rooms
Elements
Convert to linked data
12:00 21
12:10 21
12:20 22
12:40 21
:OSH_TSDB
ofo:Database
bop:isDataPointOf
Link to external DB
:Wall_02
bop:FeatureOfInterest
:Room_01
bop:FeatureOfInterest
bot:adjacentElement
:TemperatureSensor_01
bop:Sensor
:Wall_01
bop:Platform
bop:hosts
bot:adjacentElement
:M
bop:Unit
:Wall_02_Length
bop:Property
_:bn
bop:Result
bop:hasProperty
“12.0”
bop:hasPropertyState
bop:hasUnit
bop:hasValue
:Room_01_Temperature
bop:Property
:R01_T_Point
bop:DataPoint
bop:hasPropertyState
:DEG_C
bop:Unit, unit:DEG_C
bop:hasUnit
“OSH_T_0001”
bop:hasID

## Slide 16: GEOMETRY GraphDB
sparql.setQuery("""PREFIX props: <https://w3id.org/props#>
PREFIX quantitykind: <http://qudt.org/vocab/quantitykind/>
PREFIX bot: <https://w3id.org/bot#>
PREFIX bop: <https://w3id.org/bop#>
PREFIX beo: <http://pi.pauwel.be/voc/buildingelement#>
PREFIX : <https://research.tue.nl/nl/persons/alex-ja-donkers#>
SELECT ?room ?wall ?interface ?interfaceWidthValue
WHERE {
?room bop:hasSimplePropertyState "Bedroom" ;
bot:adjacentElement ?wall .
?wall a beo:Wall .
?interface bot:interfaceOf ?room, ?wall ;
bop:hasProperty ?width .
?width a quantitykind:Width ;
bop:hasPropertyState / bop:hasValue ?interfaceWidthValue
} """)

## Slide 17: TEMPERATURE GraphDB
graph_url = "http://localhost:7200/repositories/OpenSmartHomeRepository"
sparql = SPARQLWrapper(graph_url)
sparql.setQuery("""PREFIX props: <https://w3id.org/props#>
PREFIX quantitykind: <http://qudt.org/vocab/quantitykind/>
PREFIX bot: <https://w3id.org/bot#>
PREFIX bop: <https://w3id.org/bop#>
PREFIX : <https://research.tue.nl/nl/persons/alex-ja-donkers#>
SELECT ?property ?datapoint ?database
WHERE {
?room bop:hasSimplePropertyState "Bedroom" ;
bot:containsElement ?sensor .
?sensor bop:observes ?property .
?property a quantitykind:Temperature ;
bop:hasPropertyState ?datapoint .
?datapoint bop:isDataPointOf ?database .
} """)

## Slide 18: TEMPERATURE InfluxDB
client = InfluxDBClient(host='localhost', port=8086)
client.switch_database(database)
resultset = client.query(
'SELECT ‘ + property + ’ FROM ’ + datapoint + ‘ WHERE time <= ‘ + str(maxTime) + ‘ AND time > ‘ + str(minTime) + ‘ ORDER BY time DESC LIMIT 1’)
value = list((resultset.get_points(measurement=datapoint)))
temperature = value[0]['value']

## Slide 19: Results: PMV and PPD

## Slide 20: Results: PMV and PPD improvements

## Slide 21: How to integrate the occupant?

## Slide 22: Mintal
17:30:22
Kitchen
LivingRoom
Office
CO2
v
v

## Slide 23
FEEDBACK
Complaints
Likes
OCCUPANT INFO
Name
Birthday
Gender
Height
MEDICAL DATA
Sensor data measured by smartwatch
:FitbitOfJohnDoe
ofo:Smartwatch
:JohnDoe
ofo:Person, ofo:FeatureOfInterest
ofo:wears
“John Doe”
“01-12-1994”
“Male”
“1.78”
:Kitchen_ThermalComfort
ofo:ThermalComfort
:JohnDoe_Kitchen_ThermalComfort_Feedback
ofo:Feedback
ofo:hasFeedback
:JohnDoe_HeartRate
bop:HeartRate
:JohnDoe_HR_DataPoint
ofo:DataPoint
:HZ
ofo:Unit, unit:HZ
ofo:hasPropertyState
ofo:hasUnit
ofo:isPropertyOf
:JohnDoe_TCF_DataPoint
ofo:DataPoint
:UNITLESS
ofo:Unit, unit:UNITLESS
ofo:hasPropertyState
ofo:hasUnit
ofo:hasPropertyState
ofo:onProperty
LOCALIZATION
:Kitchen
ofo:FeatureOfInterest,
ofo:Location, bot:Space
ofo:hasLocation
In-app data querying
In-app RDF converter
12:00 60 Like
12:10 61 Like
12:20 65 Dislike
12:40 65 Like
:JohnDoe_TSDB
ofo:Database
ofo:isDataPointOf
ofo:isDataPointOf
Store and link to external DB
https://w3id.org/ofo

## Slide 24: Mintal resulting data structure
:JohnDoe_FitbitSense
ofo:Smartwatch
:JohnDoe
ofo:Person, ofo:FeatureOfInterest
:JohnDoeHeartRate
bop:Property
:JohnDoe_TSDB
ofo:Database
:JohnDoeHeartRateDataPoint
ofo:DataPoint
:HZ
ofo:Unit
:Kitchen
ofo:FeatureOfInterest,
ofo:Location, bot:Space
:JohnDoe_Kitchen_ThermalComfortFeedback
ofo:Feedback
:JohnDoe_Kitchen_TCF_DataPoint
ofo:DataPoint
:UNITLESS
ofo:Unit
ofo:observes
ofo:hasLocation
ofo:hasLocation
ofo:isPropertyOf
ofo:wears
ofo:hasFeedback
ofo:hasPropertyState
ofo:hasFeedbackResult
ofo:isDataPointOf
ofo:isDataPointOf
ofo:hasUnit
ofo:hasUnit
“1.78”
ofo:hasHeight

## Slide 25: Occupant Feedback Ontology (OFO)

## Slide 26: Querying with OFO
SPARQL
PREFIX ofo: <https://w3id.org/ofo#>
SELECT ?comfortProperty ?feedback ?dataPoint ?database
WHERE {
:JohnDoe ofo:givesFeedback ?feedback .
?feedback ofo:hasEvaluatedProperty ?comfortProperty .
?comfortProperty a ofo:Property .
?feedback ofo:hasResult ?dataPoint .
?dataPoint ofo:isDataPointOf ?database . }
CQ1: What active feedback is given by the occupant?
InfluxDB
USE ?database SELECT ?feedback FROM ?dataPoint ORDER BY time DESC LIMIT 1

## Slide 27: Querying with OFO
SPARQL
PREFIX ofo: <https://w3id.org/ofo#>
PREFIX opt: <https://alexdonkers.github.io/opt#>
SELECT ?personalProperty ?dataPoint ?database
WHERE {
:JohnsFitbit ofo:executesOn ?personalProperty .
?personalProperty a opt:PersonalProperty .
?personalProperty ofo:hasResult ?dataPoint .
?dataPoint ofo:isDataPointOf ?database . }
CQ2: What passive feedback is measured by the wearable?
InfluxDB
USE ?database SELECT ?personalProperty FROM ?dataPoint ORDER BY time DESC LIMIT 1

## Slide 28: Querying with OFO
SPARQL
PREFIX ofo: <https://w3id.org/ofo#>
SELECT ?feedback ?foi
WHERE {
:JohnDoe ofo:givesFeedback ?feedback .
?feedback ofo:hasFeatureOfInterest ?foi . }
CQ3: What location or object is the feedback referring to?
InfluxDB
PREFIX ofo: <https://w3id.org/ofo#>
SELECT ?location ?dataPoint ?database
WHERE {
:JohnDoe ofo:hasLocation ?location .
?location ofo:hasDataPoint ?dataPoint .
?dataPoint ofo:isDataPointOF ?database . }

## Slide 29: Querying with OFO
SPARQL
SELECT ?feedback ?result ?resultTime
WHERE {
?feedback ofo:hasResult ?result .
?result prov:generatedAtTimev ?resultTime .
BIND(xsd:dateTime(NOW()) AS ?now) .
FILTER (YEAR(xsd:dateTime(?resultTime)) >
(YEAR(?now) - 3)) }
CQ5: What feedback was given to a FOI between time t1 and t2?
InfluxDB
USE ?database
SELECT ?feedback FROM ?dataPoint WHERE time > ?t1 and time <= ?t2

## Slide 30: Querying with OFO
SPARQL
SELECT ?database ?feedback ?dataPoint .
WHERE {
:ThermalComfortPropertySet ofo:containsProperty ?property .
?property ofo:hasFeedback / ofo:isFeedbackOf :JohnDoe .
?feedback ofo:hasResult ?dataPoint . }
CQ6: What feedback is given to the properties related to a specific IEQ parameter?
SPARQL
SELECT ?database ?feedback ?dataPoint
WHERE {
:ThermalComfortPropertySet
ofo:containsProperty ?property .
?property ofo:hasFeedback ?feedback .
?feedback ofo:isFeedbackOf ?person .

## Slide 31: Querying with OFO
SPARQL
PREFIX ofo: <https://w3id.org/ofo#>
SELECT ?property ?dataPoint ?database
WHERE {
:ThermalComfortPropertySet ofo:containsProperty ?property .
{ ?property ofo:isPropertyOf :JohnDoe . }
UNION
{ ?property ofo:hasFeedback / ofo:isFeedbackOf :JohnDoe . }
?property ofo:hasResult ?dataPoint . }
CQ7: What passive feedback is measured by the wearable during the active feedback of the occupant?

## Slide 32: Property chains

## Slide 33: Integrating feedback and LBD
Perceived building performance
Measured building performance

## Slide 34: What can it do?

## Slide 35: What can it do?

## Slide 36: How to create parallel intelligence?

## Slide 37: Process
Step 1
\
\
KDD PROCEDURE

## Slide 38: Case study 1
Living room
Office space
time; ch-001; ch-002; …; ch-020; weather; outdoor temperature; outdoor wind speed; outdoor humidity; outdoor air pressure; outdoor visibility; thermal comfort feedback; air quality feedback; visual comfort feedback; building; location; floor area; room type; window/wall ratio; energylabel; occupant; heartrate; age; weight; length;
23-1-2022 17:45:00 48.85; 1.15; 2.422; Overcast; 4; 6; 81; 1034; 6; 1; 1; 0; OpenFamilyHome; LivingRoom; 52,14; LivingRoom; 0.203; A; JohnDoe; 78; 27; 72; 179;
3 weeks
2 occupants
Feedback
Sensor data
Weather data
Building information

## Slide 39: Case study 1: Comparing IEQ performance
We can compare individual building parameters as well

## Slide 40: Case study 1: Individual thermal comfort

## Slide 41: Case study 1: Individual visual comfort

## Slide 42: Case study 1: Knowledge integration
PREFIX OFH: <https://github.com/AlexDonkers/OpenFamilyHome#>
PREFIX opo: <https://alexdonkers.github.io/opo#>
PREFIX prov: <http://www.w3.org/ns/prov#>
SELECT ?firstQuartile ?thirdQuartile
WHERE { OFH:Subject1 opo:hasPreference ?preference .
?preference opo:onProperty OFH:IndoorAirQuality .
?preference prov:generatedAtTime ?time .
?preference opo:firstQuartile ?firstQuartile .
?preference opo:thirdQuartile ?thirdQuartile . }
ORDER BY DESC(?time) LIMIT 1

## Slide 43: Case study 2

## Slide 44: Case study 2: The interactive dashboard
TIPS
pop up when the measured value of a parameter exceeds predefined threshold values.
DIRECT FEEDBACK
can be given at any time to comment on the current state of a parameter (negative, neutral, or positive tag)
MICROSURVEYS
the dashboard actively asks the occupant to give feedback on random parameters to reduce bias

## Slide 45: Case study 2: Equation
Old preferred value
Preferred value
Measured value
Feedback on value
Health correction

## Slide 46: Case study 2: Results

## Slide 47: Case study 2: Results

## Slide 48: Case study 2: Personal preference models

## Slide 49: Current work

## Slide 51
John Doe, 17:00 24-06-2022
“I like this lamp!”

## Slide 52: Next up
Step 1
\
\
KDD PROCEDURE
More buildings
More occupants
More sensors
Machine learning
Actuation

## Slide 53
Ontologies
BOP: https://w3id.org/bop
OFO: https://w3id.org/ofo
Open data
Open smart home: https://github.com/AlexDonkers/ofo/tree/main/docs/OpenSmartHome
Open flat: https://github.com/AlexDonkers/ofo/tree/main/docs/OpenFlat
Open family home: on github soon
Papers
Real-Time Building Performance Monitoring using Semantic Digital Twins: http://ceur-ws.org/Vol-3081/05paper.pdf
Knowledge Discovery Approach to Understand Occupant Experience in Cross-Domain Semantic Digital Twins: https://linkedbuildingdata.net/ldac2022/files/papers/paper07.pdf
Linked Data for Smart Homes: Comparing RDF and Labeled Property Graphs: http://ceur-ws.org/Vol-2636/02paper.pdf
Creating Occupant-Centered Digital Twins Using the Occupant Feedback Ontology Implemented in a Smartwatch App [under review]: http://www.semantic-web-journal.net/system/files/swj3158.pdf
Parallel Intelligence in Semantic Digital Twins: An Interactive Decision-Support System for Indoor Comfort: email for pre-print
Automated safety checking in subway construction via semantic web technology and building information modeling [accepted]: Automation in Construction, soon online
Alex Donkers – PhD Candidate at Eindhoven University of Technology – a.j.a.donkers@tue.nl
Dujuan Yang, Bauke de Vries, Nico Baken
Resources!