## Slide 1
Using BIM for Energy-Efficient Renovation
Pierre Bourreau – Nobatek/INEF4
Nathalie Charbel (Nobatek/INEF4) – Madhumitha Senthilvel (RWTH) – Jakob Beetz (RWTH) – Nicolas Bus (CSTB) – Michel Böhms (TNO) – Jyrki Oraskari (RWTH)…

## Slide 2: Outline
BIM and Renovation
  What are the challenges
  BIM4Ren structure
  Experiment as much web semantic technologies as possible.
The BIM4Ren data model
  Need to model uncertainty – OPM
  Need to model building status
  Data access – SPARQL/GraphQL-LD/RAMOSE
The conversion process
  Based on SWRL rules
Additional features
  SHACL checkers
  A product of catalogue

## Slide 3: BIM4Ren overview

## Slide 4: BIM in Renovation
BIM is mainly used on new projects
Different depths of renovation projects
Need to digitize existing buildings (not just scanning)
Need a suitable model (IFC extension)…
Can be combined with Energy Audit interventions
Different Information for different projects
… Usable in the construction & exploitation phases
BIM and Renovation: a complementarity

## Slide 5: BIM in Renovation
BIM is mainly used on new projects
Different depths of renovation projects
Need to digitize existing buildings (not just scanning)
Need a suitable model (IFC extension)…
Can be combined with Energy Audit interventions
Different Information for different projects
… Usable in the construction & exploitation phases
BIM and Renovation: a complementarity

## Slide 6: BIM4Ren Concept
Data collection
WHAT IS THE EXISTING DATA ?
Year?
Local regulation?
Cost € ?
Energy performance?
Geometry?
Stakeholders expectations?
Type of occupants ?
Renovation potential ?
State of the existing infrastructure ?
Data Management
Data- driven design
Stakeholders involved in the renovation

## Slide 7: BIM4Ren Concept
Data collection
WHAT IS THE EXISTING DATA ?
Data Management
Data- driven design
Stakeholders involved in the renovation
To create the BIM model
To organize, consolidate, secure
To validate the BIM model
Digital inputs

## Slide 8: BIM4Ren Concept
Data collection
WHAT IS THE EXISTING DATA ?
Data Management
Data- driven design
Stakeholders involved in the renovation
Exploit BIM
To create the BIM model
To organize, consolidate, secure
To exploit the BIM model
Digital inputs

## Slide 9: BIM4Ren Concept
Data collection
WHAT IS THE EXISTING DATA ?
Data Management
Data- driven design
Stakeholders involved in the renovation
To create the BIM model
To organize, consolidate, secure
To validate the BIM model
Digital inputs

## Slide 10: Deeper view
ifcOwl
1
BIM4Ren DM
Catalogue
SHACL Checker
Conversion SPF to ifcOwl – loading to a triple store
Alignment with BIM4Ren data model
Enrichment from a LD catalogue
Checking information on models
4
3
2
1
2
3
4

## Slide 11: The BIM4Ren data model

## Slide 12: Goals
Need to model uncertainty
  ‘the composition of the external wall is certainly brick + Xcm of glass wool’
  The scan process has an accuracy of X
Need for modularity
  Different type of renovation, different depth of renovation
  Models as simple as possible
1
2

## Slide 13: Overview of the data model
https://models.bim4ren.eu
Modularity
  Independent ontologies
  3 layers (quite similar to IFC layers)
  Design pattern through multiple inheritance

## Slide 14: The Core layer
To describe specific aspects of a building, and to attach elements in it according to some specific properties
BOT: Structure of the building Goal: localize elements (‘spatially’)
SOT: Systems/network topology (MEP…) Goal: what is the role of an element within the network?
                To which elements is it directly connected?
Intervention: History of intervention Goal: keep trace of works performed (kind, criticality…)
Urban: Elements from the urban context Goal: model external masks, noise, pollution…

## Slide 15: The Product layer
To categorize building products
DistributionElements Goal: categories of products (distribution elements)
BuildingElements: Goal: categories of products (building elements)
BuildingMaterials Goal: categories of materials (for LCA, BEM…)

## Slide 16: The Domain layer
To associate specific domain properties to elements
Thermal: thermal resistance, solar factor, coefficient of performance…
Fluid: capacity, pressure…
Electrical: nominal power, power in/out…
Manufacturing: brand, product
…

## Slide 17: The Property layer
To use concepts that can be transversal to different ontologies
‘Property’: based on SML, work from CEN.
  based on QUDT (units, kinds)
  similar to OPM level 2 to add some information such as uncertainty.
Limits: uncertainty on relations (‘the insulation material of :Wall#1 may be a rockwool or glass wool’)
Next candidate: RDF*???

## Slide 18: Full Modularity
_:ElectricBoiler#1
1. What type of product is this?

## Slide 19: Full Modularity
_:ElectricBoiler#1
What type of product is this?
Where is it located?
  In the building
  In my heating network.

## Slide 20: Full Modularity
_:ElectricBoiler#1
What type of product is this?
Where is it located?
  In the building
  In my heating network.
What properties does it have?
  For a thermal study
  For an electrical study/dimensioning
  Geometrical

## Slide 21: Overview of the data model
Modularity is being discussed in bSI
Can a simple and modelling language-wide mechanism solve it (multiple inheritance)?
The model is product-centric:
  Product layer to associate a category
  Core layer to associate a building context to the product
  Domain layer to get properties (no more Property Sets…)
But frontiers are not always clear…
Need to think of a specific design pattern, understandable and easily implementable…

## Slide 22: The conversion process

## Slide 23: Why do we need conversion?
ifcOwl
1
BIM4Ren DM
Catalogue
SHACL Checker
Conversion SPF to ifcOwl – loading to a triple store
Alignment with BIM4Ren data model
Enrichment from a LD catalogue
Checking information on models
4
3
2
1
2
3
4

## Slide 24: Conversion
IFC is the most common and open standard
  We get IFCs from WiseBIM, ARtoBuild (geometry)
But IFC is quite complex => BIM4Ren model
  Relations are objectified
  Not all properties we want…
Enrich a geometric model with semantic information
  CSTB develops POBIM based on ISO23386 - Ontology
  BIM4Ren uses SML (CEN to-be standard)
CSTB: POBIM catalogue + ifcOwl
  Need to propagate changes on the BIM4Ren DM
  ifcOwl to B4R (BOT+) and POBIM to SML

## Slide 25: Different options
Static/programmatic conversion
  ++Can cover all types of elements (geometry, relations…)
  --Need save/convert/import procedure on changes
Alignment
  ++Dynamic in the triple store
  --1-1 mapping
  --Mostly covers classes, not relations

## Slide 26: Relation mappings as Inference
IFC relations are objectified
The mapping can be expressed in logic
If ?z is a bot:Zone
And ?z and ?c are connected by an ifc:relatedElements_IfcRelContainedInSpatialStructure relation
=> Then <?z; bot:hasElement; ?p>

## Slide 27: Relation mappings as Inference
IFC relations are objectified
The mapping can be expressed in logic
(?z rdf:type ?cl) (?cl rdfs:subClassOf* bot:Zone)
(?c ifc:relatingStructure_IfcRelContainedInSpatialStructure ?z)
(?c ifc:relatedElements_IfcRelContainedInSpatialStructure ?p)
=> (?z bot:hasElement ?p)

## Slide 28: Utility rules

## Slide 29: BOT rules

## Slide 30: SOT rules

## Slide 31: Product layer rules
… + ~750 rules generated with a Python script

## Slide 32: Properties

## Slide 33: Some thoughts
Multiplicity of ontologies in AEC, need to align them
Already a lot of tools that are native in web semantics (reasoning is one of them)
Conversion is dynamic
  Change on the ifcOwl model => reflected in the BIM4Ren data model
Allows one to chose its favorite vocabulary to query the model
Remark on the use of owl:OWLList instead of rdf:List
But no conversion on geometry
BIM4Ren to ifcOwl: more complex (rules are not safe)
  Use of makeTemp()

## Slide 34: Some more things

## Slide 35: BIM Models checkers
Checkers as (micro) web services
  Micro service ≤ Web service
  BIM Bots
In BIM4Ren we use SHACL checkers
  Semantic web micro services
  Semantic BIM Bots
Maestro Bot
  Orchestration service

## Slide 36: Data access
SPARQL for free
  Expert language
  0.X% of web service developers know it
REST APIs
  Easy to use
  Kind of contract between server and client
  Need to implement SPARQL Queries… tedious work (no ORM)
GraphQL-LD
  JS at either client of server
  Restricted to queries (no edition) – still?
  Kind of another expert language
RAMOSE
  Ease the deployment of REST APIs on top of SPARQL
  Also restricted to Get
  Need more work and contributions